SCRIPT : Testing Galileo signals

| Text | Images |
| --- | --- |
| 00:00:10:00 V.O. In the German Alps, Galileo is already operational before the full Galileo constellation deployment! Indeed ESA is already preparing the evolution of the European global navigation system. For this; a simulation of Galileo has been built around Berchtesgaden valley in Bavaria by DLR the German space agency. Galileo satellites are simulated by transmitters on top of the 8 highest peaks surrounding the valley. This Galileo Test and Development Environment is called GATE. | German Alps landscapes Red experimental helicopter taking off Fly around antenna containers on top of mountains |
| ITW. 00:00:45:00 Günter Heinrichs GATE project Manager, IFEN : « Because GATE is a small Galileo system on the ground, the main objectives of GATE are to enhance the Galileo receivers and Galileo equipments on early stage. |  |
| V.O . In Berchtesgaden the peaks of the mountains have therefore been equipped with different elements: transmitters and antennas with corresponding electronics in green containers playing the role of satellites. And they are emitting signals which are exact replicas of those Galileo satellites will emit from space. This set-up allows testing of several systems and technologies at once. Here a helicopter flying around the valley is used for a simulation with the precursor of Galileo; EGNOS, the European Geostationary Navigation Overlay Service which has been operational with its safety-of-life service since October 2009. For now, EGNOS is based only on filtering and correcting GPS data - but in the future it will also work with Galileo signals. The use of signals from two systems will be much more secure for air traffic... |  |
| ITW. Marc Jeannot EGNOS Navigation specialist for ESA: « Currently, it’s not possible to use GPS only for civil aviation. This is why EGNOS has been developed. It enables users to use GPS by providing correction data as well as integrity monitoring data. » « The EGNOS system is going to evolve for several reasons. It is expected to have better accuracy and an extension to new areas. Also it is expected to use new frequencies for integrity monitoring and broadcast. | Navigation specialist in front of a red helicopter. Helicopter pilot of the ESA experiment airborn. |
| V.O. Integrity is the keyword for EGNOS. For this purpose the user, the pilot, can be warned within 6 seconds, if the positions calculated are not within the specifications , for example, for landing planes or manoeuvring helicopters. | Airborn flying picture Pilot Inside the helicopter |
| ITW. Bernd Kirchgassner helicopter pilot For me as a pilot EGNOS is useful for flying in remote areas in order to find new approaches, passes or whatever and used in the offshore positions like in the windparks. All the windmills have to be approached with the helicopter and the technicians have to be brought down to the windmills. So precise systems are always appreciated. » | Pilot standing in front of his helicopter Offshore windpark. Technicians on top of an off an offshore windmill. Fly over an offshore windpark |
| V.O. Each change in position and altitude of the helicopter is recorded, the data collected will be analysed… | 2 scientists in GATE’s office watching data on computer. |
|  | Specialist in front of the red helicopter |
| V.O. By giving positions based on the redundancy of signals from two constellations the future evolution of EGNOS will be a great step forward for civil aviation. | Inside cockpit of a civil small airplane Landind small aircraft Two shot of assisted picture of landing aircraft Landing jet |
| ITW. Marc Jeannot EGNOS Navigation specialist for ESA (9660) ESA has launched the EGEP program. This program includes notably the développement (of the new version of EGNOS – which will be the EGNOS v 3-, the developpement) of new technologies for preparing the future(, and the developpement of testbeds. Among thèse testbeds, there is the High Integritiy System Testbed for which thi helicopter is used.) | Specialist in the mountain Animation 3D Berchtesgaden valley Flight assistant before take off Flight assistant from inside helicopter while take off Scientist and pilot inside helicopter while take off Helicopter elevation in the sun from outside while take off |
| V.O. By initiating its Global Navigation Satellite system Evolution Program, ESA is already preparing the future of Satellite Navigation in Europe. This means enhancing the performance of EGNOS for the Safety-of-Life Service mandatory for civil aviation and initiating the definition of Galileo second generation. END OF SCRIPT | Close up helicopter pilot airborn Fly around green container on top of mountain Scientist airborn Scientist 2 airborn Take off civile airplane from control tower airport Air shot of Marseille airport Animation of full Galileo constellation |

B ROLL

| ITW | PURPOSE |
| --- | --- |
| MARC Navigation Specialist for ESA | Landing with a GPS is possible with an aircraft? ENGL-FR |
|  | What will happen with EGNOS in the near future? |
|  | ENGL-FR |
|  | How ESA anticipates full deployment of its global navigation system? ENGL-FR |
| Bernt - helicopter pilot | How is EGNOS usefull as a pilot? ENGL-GER |
| Damien - Thalès Alenia Space | What is the use of the helicopter behind you? ENGL-FR |
|  | What is the link between this helicopter equipment and the final user of Galileo ENGL-FR |
|  | What is the context of the High Integrity Testbed? ENGL-FR |
| Günter Heinrichs GATE project Manager, IFEN | What are the main objectives of GATE? ENGL-GER |